## Slide 1: Mesure du champ de température dans une goutte d’émulsion d’eau dans l’huile par LIF-2c.
Authors:
T. Naudin(1,2), R.Calabria(1), D. Tarlet(2), P. Massoli(1), J. Bellettre(2)
(1) CNR - Istituto di Scienze e Tecnologie per l’Energia e la Mobilità Sostenibili – Naples, Italy
(2) Laboratoire de Thermique et Energie, CNRS UMR 6607 – Nantes Université, France
Journées annuelles du GDR CNRS TRANS-INTER, Aussois, 23-25 Septembre 2024

## Slide 2
  Introduction & context of the study
    Water-in-oil emulsions and its effect on combustion
    Aim of the study
  Material & methods
    2 colors Laser Induced Fluorescence technique for temperature field measurements
    Experimental bench presentation
  Results
Fluorescent dye initial characterization
Temperature dependency fluorescence Rf(T) calibration
Temperature measurements within droplets
Impact of fluid convective mixing on temperature field under radiant heating
  Discussion & perspectives
Presentation Contents
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 3
An emulsion is a blend of 2 non-miscible liquids
A small quantity of water (dispersed phase) added to a continuous phase of combustible
Stirring action to obtain a dispersion of micro-droplets of water inside the continuous phase
Addition of a component, surfactant to limit phase separation
Introduction Materials & Methods Results Conclusion & Perspectives
Introduction – General context
Generalities on emulsions systems
Oil/combustible φ
Water φ
Gain of energy by stirring
Mechanical stirrer, ultrasonicator …
Micro-channel (LteN [1])
Ji et al., Int. J. Multiphase Flow, 2020
Polar (hydrophilic) head
Non-Polar (hydrophobic) tail

## Slide 4
Emulsification of liquid fuels by the addition of a small quantity of water :
Reducing pollutants emission by chemical reactions and lowering flame temperature due to water vaporization
Increasing combustion efficiency by a secondary atomization (micro-explosion) of a W/O droplet
The atomization of the mother drop results in a cloud of « daughter » droplets, enhancing the exchange surface
Reduction of Thermal by
Reducing flame temperature
Reducing CO formation
Reducing Soot
See Abdollahi et al., Fuel 280, 2020 for example
Benefits of adding water to a combustible
General context
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 5
Continuous oily phase
dispersed water phase [5-100] μm
Vaporisation of the water droplets within the liquid oil drop
Fragmentation, forming a cloud of « child » droplets
Enhancing of combustible/air mixing and thus combustion efficiency
Micro-explosion phenomenon : atomization of a « mother » emulsion drop in a cloud of finer droplets by a difference of boiling point between the two phases composing the emulsion
The « Micro-explosion » event
What is a micro-explosion ?
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 6
Study of the behaviour of the dispersed phase and the impact of coalescence on ME
Results of previous Study
Previous study had interest on behavior of dispersed water micro-droplets by mean of LIF coupled to a PTV algorithm
It shown that for finely dispersed micro-droplets, a global motion of the droplets population exists
For coarse emulsions, the coalescence dominates and these motions are not observed
PTV results from previous study, (motions of the tracked water micro-droplets inside an emulsion drop)
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 7
A dimensionless indicator has been defined in order to characterize motion intensity of micro-droplets :
Where and are reference diameter and velocity, and the velocity and diameter of the identified droplet
Small values of I translate a high coalescence rate which ends-up in ME
High values of I result of small dispersed droplets with high velocity, which do not coalesce
Micro-droplets follow internal patterns :
A general motion, parallel streamlines that limits coalescence
Study of the behaviour of the dispersed phase and the impact of coalescence on ME
Link between internal circulation intensity and ME rate (quantified by number I)
Results of previous Study
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 8
To this aim, optical based on 2cLIF are implemented :
Allows one to obtain the full map of temperature ≠ single point measurement with a thermocouple
Non-intrusive (mainly)
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Scope of the Study
Principal objective : measurement of the 2D temperature field within a n-tetradecane droplet during the heating phase
Internal motion of the dispersed phase water has been observed
Motion induced by internal convection ?
Buoyancy induced convection ?
If yes, there should be an internal gradient inside the droplet
How the droplet is heated by IR heating ?
Bases of the problematic
Selected methods
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 9: Experimental approach
To combine non-intrusive method and obtain temperature field measurements, diagnostics based on LIF are used
Fluorescence signal is among others dependent on temperature
Ratiometric methods (measurements on 2 different wavelengths simultaneoulsy) allow one to disregard parameters
Several ratiometric methods can be used
In our case, we focused on the 2 colours 1 single dye LIF (2cLIF)
Since the study concerns the continuous oily phase of the emulsion, a coherent dye had to be choosen
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Introduction Materials & Methods Results Conclusion & Perspectives
Lemoine F. and Castanet G. (Experiments in Fluids, 2013)

## Slide 10
Setup based on 2cLIF is employed
The fluorescence light is collected on two wavelengths simultaneously thanks to a « beam-splitter » (Hamamatsu Gemini V-wiew)
First step of the work consisted on characterization of a dye suitable for our experiment :
High solubility in the liquid of interst
Can be excited by the laser wavelength (532 nm)
Sufficient temperature sensitivity and emission in the visible spectrum
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Experimental approach
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 11
Used dye : Pyrromethene 567, because of high solubility in the tetradecane
Step 1 : characterization of the absorption and fluorescence spectrums (performed in laboratory STEMS)
Plot of Fluorescence signal at only λ = 532 nm :
We observe that we have signal ranging from 510 to 650 nm  Collection bands should be selected in accordance
Absorption spectrum
Fluorescence spectrum
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Dye caracterization
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 12
Calibration of the function
A first calibration of is realized inside a Quartz cuvette
The cuvette is heated by a thermostat-controlled hotplate
Bath temperature is doubled-check with a PT100 and a thermcouple K
Fluorescence collection zone
PT 100 + thermocouple
Heated liquid bath
𝑹_𝒇 (𝑻) function (average of 4 tests)
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Exemple of fluorescence collection
Temperature uncertainty is estimated at +/- 7°C
Introduction Materials & Methods Results Conclusion & Perspectives
l1 = 550 nm, l2 = 580 nm

## Slide 13
Heating source Config. 1
Heating source Config. 2
Heating source Config. 3
3 heating configurations are studied :
TOP and SIDE case:
BOTTOM case:
Temperature selected according to a vaporization rate calibration (D²-law)
In every heating configuration, the thermal field is quite homogeneous during heating
Thus, we suggest to investigate in details the 1D temperature profiles
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Results
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 14
1D temperature profiles along the vertical axis are computed
Profiles are analyzed during the heating period of the droplet
For each configuration, temperature profiles seems rather constant
BOT CONFIGURATION
SIDE CONFIGURATION
TOP CONFIGURATION
In order to understand if the internal motion comes from buoyancy, vertical temperature gradient within the droplet is investigated
The collection band ranges from the top to the bottom of the droplet, with a width of 3 pixels (30 μm)
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Results - 1D temperature profile
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 15
Calculation of internal Rayleigh Number
Rayleigh number is then calculated inside the droplet, using the following eq. :
To this aim, the temperatures are taken in two different zones of the droplet
Illustration of the ∆T obtained in different cases
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Results – internal ∆T
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 16
Rayleigh number is then calculated inside the droplet, using the following eq. :
Variations of the physical properties (g, β, α, ν) are considered
Rayleigh number during heating and evaporation
Impact of the uncertainty of T measurements is reported
Critical Rayleigh value for the onset of buoyancy is = 1700
= 1700
Therefore, there is a contribution of the thermo-gravitational convection (buoyancy) on the internal mixing of the liquid
During all the heating phase, >
Study of the internal temperature field within an n-tetradecane droplet under radiant heating
Results – internal Rayleigh
Number
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 17
Accordingly to previous study (on water dispersed droplets), internal motion has been observed
Then, calculation of internal Rayleigh number allowed us to quantify the contribution of buoyancy on the mixing
Here, we suggest to have a glance to this mixing patterns
Link to liquid internal mixing
Results – Internal motion
Introduction Materials & Methods Results Conclusion & Perspectives
Example of internal flow within the droplet when heated by the top

## Slide 18
Presentation Contents
Two quasi symmetrical vertical vortexes are observed both by the raw images and the PTV tracking
This flow pattern is known as Hill’s Vortices (Tam et al., J.Fluid.Mech 624, 2009) and is a first indicator of a contribution of Surface Tension Forces (Marangoni) on the flow
Raw images and Post-treated results from High speed Camera at 5000 FPS
Introduction Materials & Methods Results Conclusion & Perspectives
Illustration of the internal mixing of the droplet

## Slide 19: Conclusion
2cLIF method has been sucessfully implemented in order to obtain 2D temperature field inside heated n-tetradecane droplets
3 configurations highlighting successively one type of heat transfert (convective or radiative) respect to others have been studied
In every case, temperature field seems rather homogeneous during the heating of the droplet. Plots of 1D temperature profiles also confirm this trend.
Internal Rayleigh number is calculated, depicting a contribution of the buoyancy in the liquid mixing
Next step of the work will aim to characterize the contribution of the surface tension with respect to buoyancy on the internal motion
Conclusion
Introduction Materials & Methods Results Conclusion & Perspectives

## Slide 20
Conclusion
THANK YOU FOR YOUR ATTENTION
Introduction Materials & Methods Results Conclusion & Perspectives